## Slide 1: An investigation of the screen grid tap
A search for the hidden arguments
by Rudolf Moers
ETF2022
Baarlo
The Netherlands

## Slide 2
The Ultra Linear Power Amplifier
by Rudolf Moers
ETF2010
Stella Plage
France
An adventure between triode and pentode
This lecture is a follow-up of :

## Slide 3
Contents of this lecture:
Introduction
Definitions of the screen grid tap
The AC method for optimum UL according to Rudolf Moers
The DC method for optimum UL according to Ronald Dekker
The relationship between the AC-method and the DC-method
The µTracer of Ronald Dekker in a nutshell
THD-measurement results from the past
More recent THD-measurement results
Some interim conclusions
An intermezzo: static transconductance versus dynamic transconductance
Focus not only on anode characteristic but also on transconductance characteristic
The forgotten anode dynamic transconductances
Final conclusion

## Slide 4
1. Introduction

## Slide 5
David Hafler & Herbert Keroes
(not the inventors) published
their Ultra Linear story in 1951.
Ultra Linear is a marketing name for:
Screen Grid Negative Feedback
Another name from the past is:
Distributed Load

## Slide 6
And 0.0 ≤ ≤ 1.0
Screen grid tap of the primary transformer winding : x
Why will be explaned later
In case ig2 << ia :
= 0.0 : penthode
0.0 < < 1.0 : ultra-linear
= 1.0 : triode

## Slide 7
2. Definitions of the screen grid tap
The transformation ratio is the fraction of the primary voltage and the secondary voltage:
The transformation ratio is the fraction of the secondary current and the primary current:
The fraction of the transformation impedances:
hence
Now I give these fractions their own transformation ratio:
and
Hence
Screen grid tap x is a part of n (meant is here number of windings) and 0.0 < x < 1.0 hence
The next step is rather strange but I do this because x is a part of
and a part of :
.

## Slide 9
So we achieved :
in % and
in %
When Hafler and Keroes determined that gives the lowest THD, then for those who “think in
screen grid tap in turns”, the lowest THD is at
And in the opposite way :

## Slide 10
3. The AC method for optimum UL

## Slide 12
Test circuit for measuring of all static pentode characteristics.

## Slide 17
I have repeated this excersise 6 times with:
And 6 times with and never
Known is that the lowest THD is achieved at so what do I wrong ?
Let’s see what the opinion is of Ronald Dekker, the DC-methode.

## Slide 18
4. The DC method for optimum UL
Formula of Ronald Dekker :
Translated into my notation :
http://www.dos4ever.com/uTracer3/uTracer3_pag0.html

## Slide 20
5. The relationship between the AC-method and the DC-method

## Slide 21
6. The µTracer of Ronald Dekker in a nutshell
http://www.dos4ever.com/uTracer3/uTracer3_pag0.html
Advice, visit this site
Use RS232 to USB
convertor cable to
laptop or computer
The uTracer V6 (dos4ever.com)
Advice, visit this site

## Slide 22
Graphical User Interface (GUI) running under Windows. With the GUI it is possible to set-up a measurement, and to display and manipulate the measurement data so that it is represented in exactly the same sets of curves as in the datasheets.

## Slide 23
Example of measuring a EL34 in UL-mode with x_turns = k = 0.36

## Slide 24
my µTracer
operates very
well

## Slide 25
EL84
EL34
UL animation pictures made by Ronald Dekker

## Slide 26
7. THD-measurement results from the past
← 14 May 1955

## Slide 27
Circuit used for deriving test results
Published in Radiotronics Volume 20.
Output power and THD as function
of .
Lowest THD at
15 %
or

## Slide 28
8. More recent THD-measurement results

## Slide 30
Chart: THD = f (X-turns-measured) for EL84-no.1
| 0 | 6.0000000000000032E-2 | 0.11 | 0.17 | 0.23 | 0.30000000000000032 | 0.36000000000000032 | 0.46 | 0.56000000000000005 | 0.69000000000000061 | 1
THD at 1W | 2.92 | 2.8 | 2.68 | 2.5 | 2.25 | 2.2 | 2.3 | 2.27 | 2.21 | 2.06 | 2.15
THD at 2W | 4.09 | 3.8 | 3.7 | 3.61 | 3.51 | 3.32 | 3.37 | 3.33 | 3.36 | 3.37 | 4.38
THD at 3W | 5.17 | 4.75 | 4.63 | 4.5 | 4.41 | 4.26 | 4.19 | 4.3 | 4.6
THD at 4W | 6.91 | 6.12 | 5.8 | 5.46 | 5.1 | 4.95 | 4.94 | 5.2
THD at 5W | 9.35 | 8.19 | 7.5 | 7.09 | 6.21 | 6.01 | 5.97 | 6.42

## Slide 31
Chart: THD = f (X-turns-measured) for EL34-no.1
| 0 | 6.0000000000000032E-2 | 0.11 | 0.17 | 0.23 | 0.30000000000000032 | 0.36000000000000032 | 0.46 | 0.56000000000000005 | 0.69000000000000061 | 1
THD at 1W | 1.59 | 1.05 | 0.76 | 0.55 | 0.49 | 0.5 | 0.53 | 0.63 | 0.8 | 0.91 | 1.22
THD at 2W | 3.46 | 2.53 | 1.97 | 1.46 | 1.12 | 0.87 | 0.81 | 0.85 | 1 | 1.23 | 2.58
THD at 3W | 6.08 | 4.83 | 3.77 | 2.9 | 2.23 | 1.63 | 1.3 | 1.06 | 1.11 | 2.46
THD at 4W | 9.02 | 7.47 | 6.17 | 4.74 | 3.68 | 2.72 | 2.04 | 1.72 | 2.52
THD at 5W | 12 | 10.52 | 8.97 | 7.6 | 6.47 | 4.93 | 4.41 | 3.79 | 4.21

## Slide 32
Chart: THD = f (X-turns-measured) for KT88-no.1
| 0 | 6.0000000000000032E-2 | 0.11 | 0.17 | 0.23 | 0.30000000000000032 | 0.36000000000000032 | 0.46 | 0.56000000000000005 | 0.69000000000000061 | 1
THD at 1W | 5.12 | 3.33 | 2.21 | 1.37 | 0.86 | 0.68 | 0.88 | 1.08 | 1.25 | 1.4 | 1.79
THD at 2W | 8.05 | 5.6 | 4.15 | 2.85 | 1.88 | 1.23 | 1.14 | 1.26 | 1.51 | 1.83 | 2.77
THD at 3W | 10.16 | 7.31 | 5.51 | 3.95 | 2.76 | 1.87 | 1.49 | 1.41 | 1.72 | 2.34 | 5.02
THD at 4W | 11.2 | 8.24 | 6.2 | 4.47 | 3.14 | 2.15 | 1.64 | 1.53 | 1.98 | 2.48
THD at 5W | 11.29 | 9.02 | 7.04 | 5.43 | 4.23 | 3.49 | 3.12 | 2.98 | 3.31 | 4.26

## Slide 33
9. Some interim conclusions
AC-method : most straight line in at
DC-method : most straight line in at
Measurements from the past : lowest THD at
More recent measurements : lowest THD at
So the most straight line in gives NOT the lowest THD.
Apparently there is another phenomenon that influences the THD.
Before we focus on that phenomenon we must understand the difference
between the static transconductance and the dynamic transconductance.

## Slide 34
10. An intermezzo: static transconductance versus dynamic transconductance
Static transconductances a, b, c and d in Ia = f (Vg1k) for a triode.
Dynamic transconductance (line x-w-y) in Ia = f (Vg1k) for a triode due to load line.

## Slide 35
Static transconductances a, b and c in Ia = f (Vg1k) for a pentode.
Dynamic transconductance (dashed line) in Ia = f (Vg1k) for a pentode due to a load line.

## Slide 36
Current source and voltage source equivalent circuits of a pentode with anode resistor with neglected ig2.
Voltage source and current source equivalent circuits of a triode with anode resistor.

## Slide 38
Focus not only on the anode but also on the transconductance characteristic
Tube manufactures give
hardly transconducance
characteristics for triodes and never for penthodes !

## Slide 39
Ideal transconductance characteristic and ideal
anode characteristic gives NO harmonic distortions.
Ideal transconductance characteristic and NOT ideal
anode characteristic gives harmonic distortions.
NOT ideal transconductance characteristic and ideal
anode characteristic gives harmonic distortions.

## Slide 42
I have measured at EL84, EL34 and KT88, the anode characteristic
for is respectively 0.00 ; 0.06 ; 0.11 ; 0.17 ; 0.23 ; 0.30 ; 0.36 ; 0.46 ; 0.56 ; 0.69 ; 1.00 .
These numbers are copied from the right-side column of the tabel of sheet 29 and related to my exotic output transformer.
Then I constructed for EL84, EL34 and KT88, the dynamic transconductance characteristic
for is respectively 0.00 ; 0.06 ; 0.11 ; 0.17 ; 0.23 ; 0.30 ; 0.36 ; 0.46 ; 0.56 ; 0.69 ; 1.00 .
In the next sheets I will show the forgotten dynamic transconductances !!!
But first I show the way to these results via the anode characteristic and the load line of 7000Ω.
12. The forgotten anode dynamic transconductances

## Slide 46
13. Final conclusion

## Slide 47
Order at www.boekenbestellen.nl .